## Slide 1: UV light Twitter bot
Ike Callaghan
ID620: Project 02

## Slide 2: Scope
Develop a system that routinely measures UV light.
Develop solutions to maintain 24/7 monitoring.
Use a microcontroller to communicate over the internet using an HTTP client and API service.
Program servos to provide maximum detection range for sensors.
Develop an encasing prototype.

## Slide 3: Purpose
To provide health and safety information to the local population.
Decrease skin cancer rates and UV damage.
Serve as a platform to add more environment monitoring sensors.
Develop skills in Twitter APIs and automation.

## Slide 4: Skin cancer in New Zealand

## Slide 5: Skin cancer in New Zealand
https://www.stats.govt.nz/indicators/uv-intensity

## Slide 6: Health Effects of UV Radiation
Basal cell carcinomas
Melanoma
Nonmelanoma Skin Cancers
  Basal cell carcinomas
  Squamous cell carcinomas
Premature Aging
Cataracts and Other Eye Damage
Immune Suppression
https://www.epa.gov/sunsafety/health-effects-uv-radiation

## Slide 7: Health Effects of UV Radiation
Basal cell carcinomas
Melanoma
Nonmelanoma Skin Cancers
  Basal cell carcinomas
  Squamous cell carcinomas
Premature Aging
Cataracts and Other Eye Damage
Immune Suppression
https://www.epa.gov/sunsafety/health-effects-uv-radiation

## Slide 8: Real world Applications
On-site UV index display
NIWA has developed a real time UV display in consultation with the Cancer Society and Sunsmart.
Click to add text
https://niwa.co.nz/our-services/online-services/uv-and-ozone/uvi-display

## Slide 9
https://www.rochesterfirst.com/weather/weather-glossary/uv-index-defined-what-it-means-and-how-its-measured/
Click to add text

## Slide 10: Components
9g Micro Servo: *2
NodeMCU ESP8266
XC4518 Ultraviolet Sensor
Planned Additions:
DH22 Temperature / Humidity Sensor
Air quality monitor
XC4603 Rain Sensor Module

## Slide 11: Services
IFTTTT (API platform)
Home / Mobile network
Twitter

## Slide 14: 3D models
Waterproof housing to protect main components.
Modularity for maintenance
Cable port to UV sensor housing.
Accommodates further additions.

## Slide 16: Sensor Housing
Work in progress
Requires a lot of space to accommodate servo
Requires many 'window frames' to allow for light entry.

## Slide 17: Functions
readUV()
Reads output from XC4518 sensor, converts reading to voltage. Voltage is then converted to UV index.
If the UV index reading is higher than the UV post variable, it is assigned to UV post.
spfCalc()
  Reads UV post value to decide which message to send to twitter.
  0 - 3: "apply SPF 15".
  3 - 5: "apply SPF 15+ and wear protective clothing".
  5 - 7: "apply SPF 30+ and wear protective clothing".
  7 - 10: "apply SPF 50, wear protective clothing and seek shade".
  10+: "apply SPF 50+, wear protective clothing and avoid the sun between 10am and 4pm".

## Slide 18: Functions Cont.
actionTilt()
Called after every completed pan motion. Moves the tilt servo up and down while reading UV data from readUV().
twitterRequest()
  Makes a twitter post request using an IFTTT applet.
  Posts uvPost variable from readUV() and uvMessage from spfCalc()

## Slide 19: Functions Cont.
actionPan()
  Attaches both servos to their respective pins at beginning of function call.
  Pans 90 degrees in one direction while reading UV data from readUV().
  Once panned 90 degrees, actionTilt() is called.
  The servo will make two 180 degree motions before calling spfCalc(), detatching servo motors, resetting the uvPost value to 0 and sets a delay for 1 hour.

## Slide 20: Video
Dunedin UV Bot - Video

## Slide 22: Development Constraints
Installing drivers for the ESP8266 / NODEMCU was a lengthy process for a first-time user.
The networking libraries are different on the ESP8266 compared to conventional Arduinos. To make it worse, NODEMCU ESP8266 boards have their own libraries too. A lot of research had to be put in to understand the boards.
The pin layouts on the NODEMCU were very unfamiliar to me. Using GPIO pins instead of standard digital pins.
NODEMCU Amica 3.3v input.
Connecting the ESP8266 to my home WiFi network was a nightmare.
Setting up Twitter automation was also very difficult. Twitter has changed their automation policies in recent times, making it very difficult to easily set up bots.
The tilt-pan mount I purchased from Jaycar is a bit on the cheap side, the bottom servo will often fall out if knocked around too much.
I ran into trouble with getting the correct outputs on the UV sensor. It also started smoking at some point. (I think it's ok).
API service only allows 25 packets a day for free users. Will not be a problem once fully deployed, but made it annoying to develop and test.
Hesitant to attempt any soldering, as it may affect future adaptions / developments.

## Slide 23: Future Plans
Continued maintenance for this system / API.
Addition of various sensors.
Designing and printing a specialized housing.
Plotting data over time.
Developing more Arduino API systems.
Hosting webserver for storage and display of collected data